## Slide 1: Preventive Maintenance Plans (PMPs)
IndyGo Subrecipients & Vendors
3.25.25

## Slide 2: Maintenance of FTA-Funded Vehicles
The combination of reactive & preventive maintenance aims to…
  Maximize vehicle life
  Minimize major unexpected repair costs
Assuming a service provider performs all necessary maintenance is not sufficient.
  EX: Assuming a vendor will perform all necessary preventive maintenance items when you bring in a vehicle for an oil change.
Reactive maintenance includes unplanned maintenance activities that occur in response to equipment malfunction or failure.
Preventive maintenance includes planned, routine maintenance activities that occur based on predetermined timelines.
Reactive and preventive maintenance are both required for all FTA-funded vehicles.

## Slide 3: Preventive Maintenance Plans - FTA Requirements
Per the FY24 Contractors Manual
Notes: Specific citations found at the end of the presentation.

## Slide 4
Your agency must have a written Preventive Maintenance Plan.
This plan must:
Describe a system of periodic inspections to be performed at certain defined intervals.
Describe a system of periodic preventive maintenance to be performed at certain defined intervals.
NOTE: You may employ the use of a template when drafting & updating your plan. However, the details in your agency’s PMP must accurately reflect your agency.

## Slide 5
Your plan must describe a system of periodic inspections and preventive maintenance to be performed at certain defined intervals.
Intervals are determined by your agency.
  Specific intervals are not prescribed by FTA or IndyGo.
Intervals must be compliant with Original Equipment Manufacturer (OEM) standards.
  OEM standards dictate what inspections & maintenance should be done based on mileage and/or time elapsed.
  OEM standards for maintenance are found in vehicle manuals.
  Every vehicle type & model has different standards.
Intervals are based on mileage, elapsed time, or both.
  EX: Every 10,000 miles or every 1 year, whichever comes first.
Intervals must be clearly defined.

## Slide 6
Your plan must describe a system of periodic inspections and preventive maintenance to be performed at certain defined intervals.
Intervals must be clearly defined.
EXAMPLE:
“ABC Agency will complete preventive maintenance according to OEM intervals.”
This example alone is insufficient because it is not specific.
To remedy this, ABC Agency could…
  Include clearly labeled excerpts from vehicle manuals.
    EX: ABC Agency will complete preventive maintenance according to OEM intervals, which are defined in the attached documentation.
  List maintenance activities to be performed at each mileage checkpoint for the life of the vehicle(s).
    Inspections and maintenance to be performed at 20k, 30k, 40k, etc.

## Slide 7
EXAMPLE: Schedule of Periodic Inspections & Preventive Maintenance
Notes: EXAMPLE – System of periodic inspections and preventive maintenance for a 2019 Dodge Grand Caravan.
Excerpt pulled from the 2019 Dodge GC Owners Manual - 2019 Dodge Grand Caravan Owner's Manual

## Slide 8
EXAMPLE: Checklist of Periodic Inspections & Preventive Maintenance
Notes: EXAMPLE – Checklist of periodic inspections and preventive maintenance for a 2019 Dodge Grand Caravan.
Excerpt pulled directly from the 2019 Dodge GC Owners Manual - 2019 Dodge Grand Caravan Owner's Manual

## Slide 9
Your plan must describe a system of regular & periodic maintenance checks for wheelchair lifts & ramps.
Must denote certain defined intervals.
  EX: Every 750 lift cycles or every 1 year, whichever comes first.
Must denote what maintenance activities are performed in this system.
Your plan must describe a system of regular & periodic maintenance checks for all other ADA equipment.
Must denote certain defined intervals.
Must denote what maintenance activities are performed in this system.
Other ADA equipment may include:
  Securement devices
  Signage
  Systems to communicate with persons with impaired vision or hearing
Your plan must address the Americans with Disabilities Act (ADA).

## Slide 10: Digital Maintenance Information Systems
Many agencies use a digital tool to describe their system of periodic inspections and preventive maintenance.
A digital tool used to describe & define your agency’s system of periodic inspections and preventive maintenance is sufficient.
  EX: Spreadsheet(s) containing certain defined intervals for inspections & preventive maintenance.
  Also applies to ADA equipment systems.

## Slide 11: Digital Maintenance Information Systems
If your agency chooses to use a digital tool for this purpose, note the following:
Your agency is still required to have a PMP.
  The difference is that this PMP does not outline the defined intervals, the digital tool does.
Your agency’s PMP must reference the digital tool(s) and communicate where to find the necessary information.
  EX: ABC Agency uses a spreadsheet to describe our system of periodic inspections and preventive maintenance. This spreadsheet communicates the intervals that ABC Agency has defined.
Defined intervals for periodic inspections and preventive maintenance must be available for review upon request by IndyGo.
  In other words – you must be able to efficiently share documentation of your agency’s defined intervals and what is to be performed at each interval.
Notes: If preferred, your agency may use a combination of digital & non-digital tools to describe your system of inspections and maintenance. If this is the case, clearly outline in your agency’s PMP when each tool is used.

## Slide 12
Your plan must be updated with the purchase of rolling stock.
A plan update includes:
Adding info on the specific intervals associated with the new vehicle(s)
Removing info on vehicles that have been removed from the fleet
Including an updated fleet list
Including an updated pre-trip inspection form
Reviewing the plan to ensure all info is still accurate & applicable
This accounts for:
New manufacturer’s recommended maintenance intervals
Specific intervals for each vehicle type and model
New technology

## Slide 13
Your agency must maintain a procedure for tracking warranty activities.
These procedures should aim to ensure the cost of defects is borne by the equipment manufacturer, as opposed to your agency.
FTA does not require that these procedures are included in your agency’s PMP.
  It is sufficient if warranty procedures are separate from your PMP.
NOTE: IndyGo strongly encourages that these procedures are included in your PMP. If not, warranty procedures will need to be submitted separately to IndyGo upon request.

## Slide 14
Your agency must maintain a procedure for tracking warranty activities.
This procedure must include methods to:
Identify warranty repairs.
Record warranty claims.
Submit warranty claims to manufacturer.
Follow up on unpaid claims.
NOTE: IndyGo strongly encourages that these procedures are included in your PMP. If not, warranty procedures will need to be submitted separately to IndyGo upon request.

## Slide 15
Section 5307 Vendors - Your plan must identify the goals and objectives of your maintenance program.
NOTE: For agencies that are not Section 5307, consider these best practices.
Your plan must:
Identify goals of your maintenance program.
Identify objectives of your maintenance program.
Establish how these goals & objectives will be met.
Examples of potential goals/objectives:
Increased vehicle life
Decreased frequency of road calls
Decreased maintenance costs compared to total operating costs

## Slide 16: Preventive Maintenance Plans - Best Practices
Identified by IndyGo

## Slide 17
Section 5307 Vendors - When identifying goals and objectives, consider Group TAM responsibilities…
NOTE: Per FTA, consideration of these items is not a requirement for your agency’s PM. However, IndyGo strongly encourages subrecipients to consider these responsibilities.
Consideration of these items may help determine what priorities are most important to your agency.
This includes consideration of…
  Useful Life Benchmarks (ULBs) - both age and mileage
  Condition Assessments
  Fleet Replacement Schedule

## Slide 18
When defining intervals…
NOTE: Per FTA, identification of both mileage and time is not a requirement for your agency’s PMP. However, IndyGo strongly encourages subrecipients to employ this best practice.
Identify both mileage and time intervals for vehicles.
  This practice is especially applicable if some of your agencies’ vehicles are used significantly less than others in your fleet.
  EX:
Identify both cycles and time intervals for lifts.
  EX: Every 750 lift cycles or every 1 year, whichever comes first.
Notes: Note that some OEM standards are based on both mileage and time, but not all. If your agency only identifies mileage intervals, but the OEM standard is based on both mileage AND time, IndyGo may discuss with your agency to determine best course of action.

## Slide 19
In your plan, include a discussion of…
NOTE: Per FTA, discussion of these items is not a requirement for your agency’s PMP. However, IndyGo strongly encourages subrecipients to include a discussion of some, if not all, of these items.
Maintenance-related documentation & recordkeeping procedures
  Denote specific digital programs used for record keeping.
  Denote how long records are maintained.
How your agency identifies and selects maintenance service providers
  Including if your agency works exclusively with one service provider or ‘shops around’

## Slide 20
In your plan, include a discussion of…
NOTE: Per FTA, discussion of these items is not a requirement for your agency’s PMP. However, IndyGo strongly encourages subrecipients to include a discussion of some, if not all, of these items.
Maintenance-related employee training procedures
  Denote which personnel, when, and what information is included.
  EX: Driver training occurs upon hiring and includes…
Vehicle cleaning procedures
  Denote regularity of cleaning & responsible personnel.
  EX: Weekly cleanings are performed by drivers and include…

## Slide 21
With each update of your plan, include…
NOTE: Per FTA, inclusion of these items is not a requirement for your agency’s PMP. However, IndyGo strongly encourages subrecipients to include a discussion of some, if not all, of these items.
A clear revision date
  EX: “Revised March 2025” in the header or footer of the document.
An updated copy of the fleet list
  Including make, model, year, and mileage for each vehicle.
  Identify any vehicles that have been removed from the fleet
Besides a copy of the Pre-Trip Inspection form, any other vehicle inspection forms
  Other forms may include – Post-Trip Inspection Form, Lift Inspection Form, etc.

## Slide 22: Preventive Maintenance Plans - Compliance Reviews
Performed by IndyGo

## Slide 23: Compliance Reviews
IndyGo will periodically review your agency’s PMP.
Likely once every few years to ensure compliance is maintained.
Your agency must submit a copy of your PMP to IndyGo upon request.
  If your agency uses a digital tool to describe your system of periodic inspections and preventive maintenance, this information must be shareable.
IndyGo will review to ensure your agency’s PMP…
  Contains all required elements
  Meets or exceeds OEM standards

## Slide 24: Compliance Reviews
IndyGo will periodically review your agency’s PMP. This may or may not coincide with a review of maintenance activity records.
A review of maintenance activity records typically includes:
  Submission of 2-3 years of maintenance activity records to IndyGo
  Submission of 2-3 years of warranty activity records to IndyGo
Maintenance records requests may include records from the full fleet, or records from a few select vehicles as identified by IndyGo staff.
IndyGo will review to ensure your agency’s maintenance activity…
  Meets or exceeds OEM requirements
  Includes the identification & tracking of warranty claims
  Aligns with procedures outlined in your agency’s PMP

## Slide 25: For Your Reference – Fiscal Year 2024 CORTAP Contractor Manual
Requirement | Location in Manual
Written preventive maintenance plan | Page 8-1, Question M1
Description of periodic inspection intervals | Page 8-1, Question M1
Description of periodic preventive maintenance intervals | Page 8-1, Question M1
Compliance with OEM standards | Page 8-2 & 3, Question M1
Description of periodic maintenance checks for lifts & ramps | Page 8-9, Question M3
Description of periodic maintenance checks for all other ADA equipment | Page 8-10, Question M3
Updated with purchase of rolling stock | Page 8-2, Question M1
Warranty procedures | Page 8-11, Question M4
Section 5307 - Identified goals | Page 8-2, Question M1
Section 5307 - Identified objectives | Page 8-2, Question M1
Section 5307 - Identification of how to meet goals & objectives | Page 8-4, Question M1